Reflash WiFI-modul with uStepper GUI

Install the ESP8266 package for Arduino IDE:
https://github.com/esp8266/Arduino
Board file: http://arduino.esp8266.com/stable/package_esp8266com_index.json

Download and install ArduinoWebSockets (can be downloaded through Arduino IDE) https://github.com/Links2004/arduinoWebSockets

Download and install WebOTA library manually from:
https://github.com/uStepper/ESP-WebOTA

Download and install the ESP8266 SPIFFS file uploader for Arduino (C:\Program Files (x86)\Arduino\tools): https://github.com/esp8266/arduino-esp8266fs-plugin

Connect USB to UART converter as shown below

1. Now to upload software the board needs to be in flash-mode. To enable flash-mode turn off the power to the module, and repower it while holding down the button located on the module backside. The module can now be programmed.
2. Select the board “Generic ESP8266 Module” and set the flash size to “2M (1019K OTA)”. Now Hit that upload button!’